159 Mecanum Documentation

---
float p = gyro->GetAngle();
p *= (PI / 180);
float off = (gyro->GetRate() * PI / 180) - (rotation * 2.28); //error in rotation in radians/sec
rotation = PIDLoop(.4, totalError, 0.000, 0, pError, off) * -1.0;
float diagonalA = ((1 / sqrt(2)) * (sin(theta - p) + cos(theta - p)));
float diagonalB = ((1 / sqrt(2)) * (sin(theta - p) - cos(theta - p)));
rotation *= .8;
float scalar; //intended to maximize motor output, while maintaining the same angle
if (fabs(diagonalA) + fabs(rotation) >= fabs(diagonalB) + fabs(rotation))
{
scalar = (1 / (fabs(diagonalA) + fabs(rotation)));
}
else if(fabs(diagonalA) + fabs(rotation) == 0 && fabs(diagonalB) + fabs(rotation) == 0)
{
scalar = 0;
}
else
{
scalar = (1 / (fabs(diagonalB) + fabs(rotation)));
}
//Set motor outputs by first taking diagonalA/B input and multiplying by power, then adding or subtracting rotation.
//After that we multiply by both the scalar input and .8, and then ramp the whole thing.
frontLeft->Set(ramp(((diagonalA * power) - rotation) * scalar * .8, PFL));
frontRight->Set(ramp(((diagonalB * power) + rotation) * scalar * .8, PFR));
backLeft->Set(ramp(((diagonalB * power) - rotation) * scalar * .8, PRL));
backRight->Set(ramp(((diagonalA * power) + rotation) * scalar * .8, PRR));

---
void mecDrive(float theta, float power, float rotation)
- The function takes three inputs: theta, power, and rotation (all of which should be floats)
- Theta is the angle you wish to move relative to the robot in radians
- Power is a scalar from 0-1 that you multiply your final outputs by
- Rotation is a scalar from -1 to 1 that is the desired rotation of the robot

---
float p = gyro->GetAngle();
p *= (PI / 180);
- p is the angle of the robot relative to the field
- This value is obtained from the gyro
- Since the gyro gives values in degrees and we do calculations in radians, we multiply by pi/180
- p is not required if you do not want field-centric driving (set it equal to 0 if you want robot-centric driving)

---
float off = (gyro->GetRate() * PI / 180) - (rotation * 2.28);
rotation = PIDLoop(.4, totalError, 0.000, 0, pError, off) * -1.0;
- off is the error value in radians per second
- rotation is the input that you supplied to the function. 2.28 is a constant we have based on our desired maximum angular velocity
- rotation is corrected after this with a PIDLoop based on a gyro. If you do not have a gyro do not run the PIDLoop
- We are running a custom PID loop, but you might be able to use the WPI one
- You will probably need to change the constants

---
Mecanum Math: a Primer
- We assume that wheels will apply acceleration at PI/4 and 3PI/4 to the robot.
- We assume that weight is evenly distributed across the robot, and that all wheels therefore apply identical forces at identical power levels
- We assume that there is no added friction when moving sideways as opposed to moving forwards
- Our target acceleration is power<cos(theta),sin(theta)>
- We control the accelerations of the two diagonals:
  - diagonalA(red)
  - diagonalB(green)

---
Mecanum Math (cont)
- From this, we assume that each wheel applies a vector of
  (wheelPower) <cos(wheelAngle), sin(wheelAngle)>
- sin(wheelAngle) will always be 1/sqrt(2)
- Cos wheelAngle will be +-1/sqrt(2)
- Diagonal wheels will have identical cosines and sines

---
Mecanum Math (cont)
- From this we get Xaccelnet
  =2 * cos(PI/4) * diagonalA + 2 * cos(3PI/4) * diagonalB
  =2 * (1/sqrt(2)) * (diagonalA - diagonalB)
  =sqrt(2) * (diagonalA – diagonalB) = power(cos(theta))
- And Yaccelnet
  =2 * sin(PI/4) * diagonalA + 2 * sin(3PI/4) * diagonalB
- =sqrt(2) * (diagonalA + diagonalB) = power(sin(theta))

---
Mecanum Math (cont)
- Then we subtract the Y from the X and get:
  Sqrt(2) * (-2 * diagonalB) = power * (cos(theta) – sin(theta))
  so diagonalB =
  (½ * sqrt(2)) * power * (sin(theta) – cos(theta))
- Then we add X to Y and get:
  sqrt(2) * (2 * diagonalA) = power * (cos(theta) + sin(theta))
  So diagonalA=
  (1/2*sqrt(2)) * power * (cos(theta) + sin(theta))

---
Mecanum Math (cont)
float diagonalA = ((1 / sqrt(2)) * (sin(theta - p) + cos(theta - p)));
float diagonalB = ((1 / sqrt(2)) * (sin(theta - p) - cos(theta - p)));

---
Scalar fun for everyone
Still with us? Good! You may have noticed that our math so far results in outputs that look like this:

---
Scalar Fun (cont)
- Obviously, this isn't exactly efficient- when going straight forward or backward we should be able to just set both diagonals to max, instead of only partway
- To do this, we use a scalar. Essentially our objective here is to make the diagonal with the biggest magnitude end up with a magnitude of 1, and scale the other diagonal accordingly to maintain the same final direction.

---
Scalar Fun (cont)
- We determine which diagonal will be used in computation of the scalar by adding the rotation to both diagonalA and diagonalB, and then calculating which is bigger
- We compute the scalar by taking the inverse of the absolute value of the diagonal plus the rotation
- If both diagonalA plus rotation and diagonalB plus rotation are equal to 0, we set the scalar to 0

---
Scalar Fun (cont)
if (fabs(diagonalA) + fabs(rotation) >= fabs(diagonalB) + fabs(rotation))
{
   scalar = (1 / (fabs(diagonalA) + fabs(rotation)));
}
else if(fabs(diagonalA) + fabs(rotation) == 0 && fabs(diagonalB) + fabs(rotation) == 0)
{
   scalar = 0;
}
else
{
   scalar = (1 / (fabs(diagonalB) + fabs(rotation)));
}

---
An explanation of rotation
- We get rotation by adding a value to the left side of the robot and subtracting it from the right side of the robot
- It is similar to tank drive in this regard
- If you're using a gyro, you can run a PID loop with rotation using the gyro as a way to get error instead of feeding in a value from zAxis directly

---
An explanation of rotation (cont)
An example of using the gyro for a PID loop (reposted from above in case you forgot)
float p = gyro->GetAngle();
p *= (PI / 180);
float off = (gyro->GetRate() * PI / 180) - (rotation * 2.28);
rotation = PIDLoop(.4, totalError, 0.000, 0, pError, off) * -1.0;

---
Ramping
- Sometimes drivers will be crazy-it happens to even the sanest of people
- Attempting to rapidly change the direction of a wheel is VERY VERY BAD for the gearboxes/axles/mechanical components of a bot
- To reduce the amount of jerk applied to mechanical pieces we can raise the response time of the drive code through ramping
- Just take the weighted average of the current desired power and the previous desired power and feed that in instead (We use .7 current + .3 previous)

---
Putting it all together
- Now we multiply diagonalA and diagonalB by power and add or subtract rotation
- We then multiply by the scalar
- This total is then fed into the ramping function before finally going to the motor
frontLeft->Set(ramp(((diagonalA * power) - rotation) * scalar * .8, PFL));
frontRight->Set(ramp(((diagonalB * power) + rotation) * scalar * .8, PFR));
backLeft->Set(ramp(((diagonalB * power) - rotation) * scalar * .8, PRL));
backRight->Set(ramp(((diagonalA * power) + rotation) * scalar * .8, PRR));