Simulated Robot
For FRC 2017 “Steamworks” Game
Team 159
# Motivation
## Overview
As was the case for the previous two seasons a Gazebo simulation project was developed in parallel with the team’s competition robot code for this year’s “Steamworks” game. Using the simulation tools provided by First has the following benefits:
- The ability to test the inertial and geometry properties of a model as in interacts with a problems in a simulated FRC field without needing to construct a working robot and physical field elements
- The ability to test and develop software used to control a robot model prior to the availability of a working prototype
- A mechanism to continue testing software and competition strategies between bag day and the days of competition
- A way to explore new sensor technologies (e.g. image recognition) and subsystem ideas (e.g. special drive-trains or manipulators) during the off-season
# Tools and Resources
## Components
The current simulation environment supported by First includes the following principle components:
Solidworks “sdf” exporter
An application “plugin” that is used to produce a set of files from a Solidworks model that can be exported to the Gazebo simulator
Eclipse linux_simulation build
A special Eclipse build configuration that generates a “FRCUserProgram” binary from robot software source code that runs in the Gazebo simulation environment
Gazebo simulator
Provides a graphical simulation environment to test the interaction of the mechanical model created with the Solidworks exporter and the Software model created from the Eclipse linux_simulation build
GRIP vision processing subsystem
  - GRIP was introduced last year as a Java based application that could be used to set up a series of filters and other functions in order to process images from a camera to isolate targets in the competition field for autonomous mode challenges or auto-assisted teleop targeting
  - It was designed as a replacement for NI’s proprietary “NIVision” subsystem which was neither free (outside of First teams use) nor open sourced
  - The Java based version was often found to be too slow when running on the RoboRIO arm processor and also required installing a significant number of third party libraries (Java-8, JavaFX etc.). So this year the recommended deployment method is to use a special tool in the GRIP user interface to generate native opencv source code (Java, C++ or Python) and then port that code to the target platform (e.g. by direct compilation into the robot program)
  - In order to get this new approach working with the gazebo simulator (running in a Linux environment) is was necessary to first build several components from source (cscore, CameraServer etc.) that were supported by pre-compiled arm libraries when deployed on the Roborio but were not available for simulation. (A separate write-up about going about this is available on the MentorRepository github site:FRCSimulation2017.odt)
# Solidworks
## Models
1. Robot
  The team’s Solidworks robot model was completed fairly early this year so a useful simulation prototype was available to test autonomous strategies etc. using software models well before the end of the build season.
2. FRC Field
  Unlike in previous years, a simplified Gazebo model for the competition field wasn’t provided by First this season so it was instead necessary to generate a facsimile of the field by exporting a Solidworks CAD design that was made available as a free download. However, owing to the large size and complexity of the field model (even after removing several components and “defeaturing” it in Solidworks) if was found to be necessary to also disable the collision property of most of the elements that were not directly required to test the behavior of the robot model’s interaction with the field. The collision components retained included the target “spikes” and gear placement front panels
3. Gear
  A Solidworks assembly for the Gear was available as part of the Field download mentioned above and was exported as a separate model using the Solidworks Gazebo sdf exporter
  - The compression properties were modified to reduce the hardness of the surface so that the collision with the “harpoon” spring was more accurately modeled
1. Balls (Fuel)
  A simple 5” diameter yellow sphere was generated as a Solidworks assembly and exported using the Gazebo exporter plugin
2. Vision Targets
  A Solidworks sketch of the Gear placement target pattern was created (two 2x5” strips separated by 10.5” outside edges)
  - The dual tape models were place on the field panels directly behind the spikes and were suspended in place by setting gravity to zero in the Gazebo model
  - The color was changed to best match the color of the reflective tape illuminated by a green light ring
  - The tape was also given a certain amount of “emission” property and the ambient lighting of the Gazebo scene was reduced to better emulate the conditions seen by the targeting camera
## Competition Robot
The final robot design included an 8 wheel drive train with a pneumatic switch to select between a low and high gear ratio, a bumper subsystem and two manipulators: A fuel pusher subsystem that was designed to load balls contained in a hopper into the lower intake slot of the boiler and a rope climbing mechanism composed of a hook and spindle. A release plate was also designed to allow the gear to drop free of side constraints after it was placed on the spike.
## Simulated Robot
### Components Modeled
The following components were modeled in simulation:
- An 8 wheel drive train with dual speed transmission
  - Selected by 2 buttons (high,low)
- A ball pusher subsystem consisting of a linear actuator
  - Activated by a button
- A mechanism to release a gear after placement on the spike
  - Activated by a button (teleop) or automatically opened at the end of autonomous
- A vision based auto-targeting subsystem for autonomous mode
- A secondary driver camera for teleop mode
- An ultrasonic sensor for distance measurement
- A simulated gyro to measure turn angle
### Components not Modeled
- Electronics board,pneumatics, battery and wiring
- Rope climbing subsystem
### Simulation problems and workarounds
Because of limitations in the current Solidworks exporter and Gazebo simulator some of the mechanical and sensor components couldn't be modeled
1. The rope climbing subsystem couldn’t be modeled because the gazebo simulator doesn’t directly support deformable objects such as springs and cables
2. The simulated ultrasonic sensor was found to be unreliable (sometimes returning inaccurate or even negative values) and so was not used in simulation
### Screen-shot of final simulated robot
Final Solidworks Model of Simulated Robot

### Solidworks Exporter Robot Model Joint tree

Right (Top) Frame (non-articulating side) and right wheels

Sensors: Gyro(yaw), Rangefinder (ball detector), Encoder(on R2Wheel)

Left Frame (articulating side) and left wheels
To Top Frame
Sensors: Encoder(on L2Wheel)

Ball Loader (contains 5 rollers – 2 not shown)
To Top Frame
Sensors: Gyro-pitch (emulates accelerometer), Camera (rear facing), Lower Limit switch on arm

Shooter/Holder
To Top Frame
Shooter Sensors: Camera (front facing), Gyro (emulates accelerometer), Rangefinder(emulates Lidar)
Holder Sensors: Encoders (left&right flywheels) Limit switches (gate open, closed)

### Sources
The Solidworks design files that were used in the 2017 Simulated Robot are available in the github repository “Team159/MentorRepository” in the sub-directory Solidworks/Models/
https://github.com/FRCTeam159/MentorRepository/tree/master/Solidworks/Models/2017-SimRobot
The “.sdf” and mesh files generated by the Solidworks exporter are also available for deployment in the Gazebo simulator and can be downloaded from the Solidworks/Exported/FRC2017_Exported directory in the Team159/MentorRepository:
https://github.com/FRCTeam159/MentorRepository/tree/master/Solidworks/Exported/FRC2017_Exported
# Software
## Software paradigms
The First/WPI enhancements to the Eclipse IDE provide an opportunity to base a Robot design using either the “Integrated” or “Command” style paradigms.
The “Integrated” paradigm is arguably the simplest to implement since it runs in a single thread with direct callbacks from the user's code to the state machine that services periodic (20 ms) control updates in Teleop and Autonomous modes. A disadvantage of this approach is that the user code needs to be aware that it is running in a scheduler and so cannot monopolize compute resources in a given update cycle while servicing a single program aspect (like the PID control of a motor, or an image processing step) without running the risk of degrading another critical function (such as joystick control over the drive-train).
The “Command” paradigm is somewhat more complex since it requires that the source code be more carefully organized into separate classes that extend the Command and Subsystem library base classes. The “Commands” in the user program can be designed to carry out simple operations such as to toggle a lever, raise a manipulator by a fixed amount or more complex operations such as to direct a state machine that controls an entire subsystem. Commands can also be configured to run sequentially or in parallel and can be strung together into “CommandGroups” that can be used to specify a complex series of operations that might be used, for example, to implement an Autonomous mode strategy
## Competition Robot Project Software
The 2017 Competition software was c++ based and was developed by the students using the Eclipse Integrated Development Environment (IDE) with plug-ins provided by First and WPI that are used to generate binary files that run (as applications) on the RoboRio's embedded Arm processor.
The overall software design included independent state machines for three separate subsystems as well as a vision based auto-targeting system. Software control was needed for 6 motors, 2 cameras, a Ultrasonic Rangefinder, 2 encoders (on the drive wheels) and 2 limit switches. Extensive use was made of tuned PID control loops
Code development was carried out in the Windows(10) operating system environment which allowed for direct deployment of the compiled binary file from Eclipse to the robot hardware over wireless Ethernet. This year the team also made extensive use of the Java based “SmartDashboard” application particularly for tuning the camera and targeting parameters used for autonomous operation.
### Paradigm
This year's software was based on the “Command” paradigm
### Architecture
Following the “Command” paradigm the software design was centered around several subsystem classes, each with a special “default” command that controlled the subsystem’s operation during Teleop mode
Mechanical subsystems included a drive train controller (DriveTrain), fuel delivery system (FuelSubsystem), gear delivery system (GearSubsystem) and climber (ClimbingSubsystem).
A separate subsystem class was also created for the ultrasonic rangefinder (UltraSonicSubsystem)
Vision based targeting employed it’s own subsystem class (Vision) as well as a separate Utility class (GripPipeline) that was a modified version of the c++ snippit produced by the GRIP application after tuning it to segment retro-reflective tape illuminated by a green led ringlight. The GripPipeline class was executed in a separate thread from the main robot application and was responsible for carrying out the image processing operations on the camera input stream using native OpenCV library calls running on the RoboRio. Communication between the GripPipeline and Vision application was done using NetTables PutNumber and GetNumber calls.
### Implementation Details
### Code sources
Source code is available for viewing or download from the “HughBot” project in the github Team159/2017-Robot-Code repository directory at:
https://github.com/FRCTeam159/2017-Robot-Code
## Simulation Robot Project Software
The source code used in this year’s simulated robot project (SimHughBot) was almost identical to that employed for the competition robot. In many cases the student’s code was simply copied over and recompiled using the linux_simulate build target. The following differences however are noted:
- Since simulation classes for CANTalon motor controllers have never been supported by WPI a separate project was developed (CANTalonLib) to allow most of the functionality of those controllers to be emulated. Source code for this library is available on line at the team’s MentorRepository github site.
- The digital gyro used in the competition robot was emulated using the simulated AnalogGyro class
- Several bugs and other problems exist in the current WPI simulation libraries (e.g. see section 3.3 below). These were fixed in the allwpilib code and the library was rebuilt
### Software paradigm
As for the competition code this year's simulation software was also based on the “Command” paradigm
### Code resources
Source code is available for viewing or download from the “SimHughBot” project in the github Team159/MentorRepository repository directory at:
https://github.com/FRCTeam159/MentorRepository/Software/workspace/ SimHughBot
### Patches for WPI library bugs
#### PIDController and Notifier classes
Last year several problems were discovered in the simulation code related to PIDControllers.
A bug report (artf4830) was submitted for these problems though the TeamForge website on 3/15/2016 and has been assigned for work with the status “Open”. Progress can be tracked at the following URL:
https://usfirst.collab.net/sf/go/artf4839?returnUrlKey=1460655219989
#### Talon and Victor classes
In the simulation build neither of the older motor controller classes return a non-zero value for the Get or GetSpeed functions (which was found to be important when trying to combine multiple PID controllers). This problem appears to have a very simple fix (a class variable was just not getting updated) and a Bug report was submitted on 3/17/2017 and can be tracked at:
https://usfirst.collab.net/sf/go/artf4840?returnUrlKey=1460655771424
Update: as of 3/2017 no work appears to have been done at WPI to fix any of these reported problems
## Launching a simulation
Although there is supposedly a plan in the works to provide Windows support in the future, simulations currently need to be carried out in a Linux (specifically Ubuntu) OS environment. Details on how to set up a virtual or native Linux environment with all the necessary support tools have been described in a previous report so wont be repeated here. However, a good reference on how to get started with this can be found at the following link: http://wpilib.screenstepslive.com/s/4485/m/23353
The procedure for running a simulation for this year is:
Execute one of the 3 start-up scripts located in the SimHughBot project directory
> cd ~/Robotics/MentorRepository/Software/workspace/SimHughBot
> ./start_simulation-center
or:
> start_simulation-right
or:
> start_simulation-left

Each of these scripts will cause the following series of applications or command scripts to be launched in separate “roxterm” tabs:
  - start_gazebo_<center,left,right>
    - starts command script: gazebo-2017-field-<center,left,right>
    - starts up gazebo application with center,left or right “.world” file
  - start_targeting_camera
    - starts up “mjpg_streamer” application for targeting camera
  - start_driver_camera
    - tarts up “mjpg_streamer” application for driver camera
  - FRCUserProgram
    - executes simulation robot program in S../SimHughBot/linux_simulate
  - sim_ds
    - starts up simulation driver-station Java application jar file in ~/wpilib/tools
  - start_smartdashboard
    - starts up Java “SmartDashbord” jar file in ~/wpilib/tools
# Tests and Results
### Tests and Observations

Driving and turning
- The general responsiveness to accelerating and turning of the robot model in the simulator was seen to be more sluggish than that observed in the real robot. Some of the difference can probably be attributed to the fact that the simulation runs at a fraction of real-time speed and therefore is somewhat moving in “slow motion”.
- Responsiveness was also improved by running the simulator on a system with a faster processor and graphics card (e.g. as opposed to a slow laptop or from within a virtual machine)
Cameras
- In the Gazebo simulator it's possible to both project a view seen from a camera to a “floating screen” in the field and/or to a separate window that can be made visible through a selection in the “Topic Visualization” menu list
- Two cameras were added to the Simulated robot in similar locations to those placed on the physical robot and it was possible to view the field from the perspective of either camera by switching between topics in gazebo.
  - Separate panels for each camera are are also included in the “SmartDashbord” interface
### Screenshots
Robot Model in Gazebo

Starting Position Center

Starting Position Right

Starting Position Left

After Successful Autonomous (Right)

SmartDashboard Screenshot